## Slide 1
Datetime | Load
2023-02-03 10:00:00Z | 8.2
2023-02-03 10:15:00Z | 8.6
… | …
Windspeed | APX | E1C_AMI_A | …
3.2 | 48.0 | 0.0012 | 
3.8 | 48.0 | 0.0015 | 
… |  |  | 
Load 2days before | Load 15 mins before | Wind Energy | Dew-point | isWeekday | …
14.3 | 7.8 | 0.20 | 8.9 | 0 | 
14.6 | 8.2 | 0.23 | 9.1 | 0 | 
… |  |  |  |  | 
Load
Weather Forecasts
Market Prices
Typical Profiles
Derived Weather
Derived Renewable
Lagged Load
Target – y
External Predictors
Derived Features
Features - x
Input Backtest Pipeline
Calculates
Multiply for training horizons
Datetime (excl in fit) | Load | Windspeed | APX | E1C_AMI_A | … | Load 2days before | Load 15 mins before | Wind Energy | Dew-point | … | Horizon (excl. in fit)
2023-02-03 10:00:00Z | 8.2 | 3.2 | 48.0 | 0.0012 |  | 14.3 | 7.8 | 0.20 | 8.9 |  | 0.25
2023-02-03 10:00:00Z | 8.2 | 3.2 |  | 0.0012 |  | 14.3 |  | 0.20 | 8.9 |  | 47.0
2023-02-03 10:15:00Z | 8.6 | 3.8 | 48.0 | 0.0015 |  | 14.6 | 8.2 | 0.23 | 9.1 |  | 0.25
2023-02-03 10:15:00Z | 8.6 | 3.8 |  | 0.0015 |  | 14.6 |  | 0.23 | 9.1 |  | 47.0
… |  |  |  |  |  |  |  |  |  |  | 
1) OpenSTEF forecasts a timeseries with a known history; the Target. Typically this is the measured load on an asset.
Calendar Info
2) The Target is merged with External Predictors, such as Weather Forecasts.
3) Derived Features are calculated, such as the Lagged Target, weekday and the generation of a typical wind turbine
4) OpenSTEF trains a single model to predict the load at all lead times. This is performed by duplicating the training data for every training horizon (typically 15 minutes ahead and 47 hours ahead), and masking all features which are operationally not available at that training horizon. E.g. The day-ahead electricity price is known for a training horizon of 15 minutes, but not for 47 hours. This way, the model has increased predictive power for short lead times, while also able to make a sensible prediction at long lead times
model.fit
4) During Forecasting, the model predicts in a single shot all requested lead times, typically up to 48 hours ahead with a 15 minute resolution.
Wind-speed | APX | E1C_AMI_A | … | Load 2days before | Load 15 mins before | Wind Energy | Dew-point | …
4.2 | 52.0 | 0.0013 |  | 5.2 | 5.1 | 0.60 | 7.1 | 
4.4 | 52.0 | 0.0013 |  | 5.7 |  | 0.68 | 7.3 | 
8.8 |  | 0.0015 |  | 5.1 |  | 0.88 | 7.1 | 
model.predict
Datetime | Load Forecast
2023-02-04 07:00:00Z | 7.6
2023-02-04 07:15:00Z | 7.8
… | 
2023-02-05 06:45:00Z | 7.4
Datetime
2023-02-04 07:00:00Z
2023-02-04 07:15:00Z
…
2023-02-04 06:45:00Z
Forecast @ 2023-02-03 06:50:00Z

## Slide 2
Load
External Predictors
Weather forecasts
Derived Features
Windspeed
Radiation
Temperature
…
Market Prices
Day Ahead Electricity
…
Typical Profiles
Household with PV
Business
…
Derived Weather features
Derived Renewable
Global Tilt Irradiance
Dewpoint
…
Typical Solar Park
Typical Wind Turbine
Calendar
IsWeekday
IsHoliday
…
Target
Household
Lagged Load
Load two days before
Load 15 minutes before
…